## Slide 1: MIPS Processor Project Presentation
ECE 4120/5120 - Spring 2025
Team: Matthew Collins & Lewis Bates
Emails: mcollins42@tntech.edu & lfbates42@tntech.edu

## Slide 2
Final Working Project
Achievement: Successfully implemented a single cycle processor (Fig. 1), and a pipelined MIPS processor (Fig. 2), with the exception to a data memory error. We attempted the Bonus Pipeline processor with Forwarding and Hazard Units (Fig. 3); When tested, there were errors present.
Details:
  Integrated all three phases for a complete single-cycle implementation (Fig. 1).
  Extended to a simple pipelined architecture (Fig. 2).
  Added bonus features: forwarding unit for data hazards and hazard unit for load-use hazards (Fig. 3).
Outcome: Demonstrated correct execution of MIPS instructions, including branching, data hazards resolution, and pipelining efficiency.

## Slide 3
Initialization and Setup
Register Values:
  Method: Loaded using addi instructions via the test bench.
  Values: $t1 = 1, $t2 = 2, $t3 = 3, $t4 = 4.
  Rationale: Chosen to create data dependencies and test forwarding (e.g., between add and subsequent instructions).
Data Memories:
  Method: Loaded using .mif files in ModelSim-Altera.
  Values: memory[8] = 20, memory[100] = 0 (initially).
  Rationale: Specific addresses to verify lw and sw operations, with memory[100] updated by sw.
Instruction Memories:
  Method: used the testbenches to load the instruction memory with machine code.
  Instructions:
    beq $t1, $t2, Equal (000100 01001 01010 0000000000000100)
    lw $t1, 8($t2) (100011 01010 01001 0000000000001000)
    add $t2, $t1, $t2 (000000 01001 01010 01010 00000 100000)
    sw $t3, 100($t2) (101011 01010 01011 0000000001100100)
    add $t4, $t1, $t2 (000000 01001 01010 01100 00000 100000)
  Rationale: Tests branch (not taken), load-use hazard, forwarding, and store functionality.

## Slide 4
Single Cycle Implementation Results
Key Results:
  beq $t1, $t2, Equal: Not taken ($t1 = 5, $t2 = 10, not equal).
  sw $t3, 100($t2): Successfully stores $t3 = 15 into memory[100].
Verification:
  ALU zero flag = 0 for beq.
  Data memory output shows memory[100] = 15.
Screenshot Needed: Waveform from ModelSim-Altera showing single-cycle execution, highlighting beq zero flag and sw memory update.

## Slide 5
Pipelined Implementation Results
Key Results:
  Demonstrated pipelining across fourth, fifth, and sixth clock cycles.
  Cycle 4: lw $t1, 8($t2) completes, $t1 = 20.
  Cycle 5: add $t2, $t1, $t2, $t2 = 20 + 10 = 30.
  Cycle 6: sw $t3, 100($t2) stores 15 at updated address.
Verification:
  ALU outputs and data memory values match expected results.
  Improved throughput vs. single cycle.
Screenshot Needed: Waveform showing cycles 4-6, with ALU outputs ($t2 = 30) and data memory (memory[100] = 15).

## Slide 6
Bonus Part - Forwarding and Hazard Units
Forwarding:
  Between add $t2, $t1, $t2 and add $t4, $t1, $t2: $t2 forwarded, $t4 = 20 + 30 = 50.
  Between add $t2, $t1, $t2 and sw $t3, 100($t2): $t2 forwarded for address calculation.
Hazard Unit:
  Between lw $t1, 8($t2) and add $t2, $t1, $t2: Stall inserted, bubble prevents incorrect $t1 use.
Screenshot Needed: Waveform showing forwarding (e.g., $t2 to add $t4) and hazard stall (bubble after lw).

## Slide 7
Demonstration Notes
Tool: ModelSim-Altera.
Waveforms:
  Single cycle: Show beq and sw.
  Pipelined: Show cycles 4-6.
  Bonus: Show forwarding and hazard stalls.
Preparation: Waveforms pre-loaded on laptop for immediate display post-presentation.